## Slide 1: EEE 109 Electrical Circuits
Dr. Md. Forkan Uddin
Associate Professor
Department of Electrical and Electronic Engineering (EEE)
Bangladesh University of Engineering and Technology (BUET)

## Slide 2: Network Theorems
Boylestad – Chapter 9

## Slide 3: Topics to be Covered
Superposition Theorem
Thevenin’s Theorem
Norton’s Theorem
Maximum Power Transfer Theorem

## Slide 4: Superposition Thorem
The current through, or voltage across, an element in a linear bilateral network is equal to the algebraic sum of the currents or voltages produced independently by each source
Deactivating Sources:
Voltage Source: Short Circuit
Current Source: Open Circuit

## Slide 5: Superposition Principle
Example: Calculate I1

## Slide 6: Superposition Principle: Power
Superposition Principle is not true for calculating power (as power is a non-linear quantity of voltage or current)
Proof:
On the other hand,
(if PT had followed superposition)

## Slide 7: Thevenin’s Theorem
Any two-terminal, linear bilateral dc network can be replaced by an equivalent circuit consisting of a voltage source and a series resistor
VTh = Thevenin Voltage
RTh = Thevenin Resistance

## Slide 8: Thevenin’s Theorem
Usefulness of Thevenin’s Theorem
allows us to find any particular voltage or current in a linear network with one, two, or any other number of sources
we can concentrate on a specific portion of a network by replacing the remaining network with an equivalent circuit.

## Slide 9: How to find Thevenin Equivalent Circuit?
Procedure
1. Remove that portion of the network across which the Thevenin equivalent circuit is to be found
2. Mark the terminals of the remaining two-terminal network
3. Calculate RTh by first setting all sources to zero and then finding the resultant resistance between the two marked terminals
4. Calculate ETh by first returning all sources to their original position and finding the open-circuit voltage between the marked terminals
5. Draw the Thévenin equivalent circuit with the portion of the circuit previously removed replaced between the terminals of the equivalent circuit
RTh
RL = 5 ohm
Iab = ?
Vab = ?

## Slide 10: Thevenin Equivalent Circuit
ETh
Thevenin Equivalent Circuit
Iab = - 0.6 A
Vab = - 3V

## Slide 11: Norton’s Theorem
Any two-terminal, linear bilateral dc network can be replaced by an equivalent circuit consisting of a current source and a parallel resistor
IN = Norton Current
RN = Norton Resistance
Converting between Thevenin and Norton equivalent circuits

## Slide 12: Norton’s Theorem
Procedure
1. Remove that portion of the network across which the Norton equivalent circuit is to be found
2. Mark the terminals of the remaining two-terminal network
3. Calculate RN by first setting all sources to zero and then finding the resultant resistance between the two marked terminals
4. Calculate IN by first returning all sources to their original position and finding the short-circuit current flowing between the marked terminals
5. Draw the Thévenin equivalent circuit with the portion of the circuit previously removed replaced between the terminals of the equivalent circuit
RN

## Slide 13: Norton’s Theorem
IN
Norton Equivalent Circuit

## Slide 14: Maximum Power Transfer Theorem
A load will receive maximum power from a linear bilateral dc network when its total resistive value is exactly equal to the Thevenin (Norton) resistance of the network as “seen” by the load

## Slide 15: Maximum Power Transfer Theorem
Proof

## Slide 16: More on Maximum Power Transfer Theorem

## Slide 17: More on Maximum Power Transfer Theorem
Efficiency and Maximum Power Transfer Theorem
Efficiency is increasing, but power at load is decreasing.
Is it contradictory?

## Slide 18
Efficiency and Maximum Power Transfer Theorem

## Slide 19: Maximum Power Transfer Theorem
Example
Determine the value of R for maximum power to R, and calculate the power delivered under these conditions.