## Slide 1: Continuous-Time Systems
Waselul Haque Sadid
Assistant Professor

## Slide 2: Linear and Nonlinear Systems
Let x1(t) and x2(t) be the inputs and y1(t) and y2(t) be the response to x1(t) and x2(t)
The system is linear if
  The response to x1(t)+x2(t) is y1(t)+y2(t)
  The response to x1(t) is y1(t)
  x1(t)+x2(t) y1(t)+y2(t)
    x(t)y(t) represents the input/output relation of a continuous system
  Example: 2.2.1, 2.2.2

## Slide 3: Time-Varying and Time-Invariant
A system is time invariant if a time shift in the input signal causes an identical time shift in the output signal
If y(t) is the response for an input x(t), then a time-invariant system will have an output y(t-t0) for the input x(t-t0)
To verify whether a system is time-invariant:
  y1(t) be the output for x1(t)
  Consider another input x2(t) as x1(t-t0)
  Find y2(t) corresponding to x2(t)
  Find y1(t-t0) and compare with y2(t)

## Slide 4: Systems with Memory
The inputs and outputs are functions of the independent variable for most of the systems
A system is memoryless or instantaneous if the present value of the output depends only on the present value of the input
Example 1
  A resistor is memoryless
  If the input x(t) is current and the output y(t) is voltage, then the input/output relationship is
  y(t) = Rx(t), where R is a resistance
  The value of y(t) at any instant depends only on the value of x(t) at any instant

## Slide 5: Systems with Memory
Example 2
  A capacitor is a system with memory
  With input x(t) as the current and output y(t) as the voltage, the input/output relationship is
  , where C is the capacitance
  The output at any time t depends on the entire past history of the input

## Slide 6: Systems with Memory
The input/output relationship for the memoryless system can be written as
y(t) = Fx(t)
The relation for the linear systems reduces to
y(t) = k(t)x(t)
If the system is time-invariant, then
y(t) = kx(t)
Example:
  Mechanical damper is a linear, time-invariant, memoryless system
  Linear dependence between force f(t) and velocity v(t)
  , where D is the damping constant

## Slide 7: Causal Systems
A system is causal or nonanticipatory if the output at any time t0 depends only on values to some time t0
If two inputs to a causal system are identical up to some time t0, the corresponding outputs must also be equal up to the same time
A causal system cannot predict
If two inputs x1(t) and x2(t) are mathematically identical up to t0, i.e., x1(t)=x2(t); t< t0
And if the system is causal, then y1(t)=y2(t); t< t0
A system is noncausal or anticipatory if it is not causal

## Slide 8: Inverse Systems
A system is invertible if we can determine the input by observing its output
The inverse system undoes what the given system does to input x(t)
System
Inverse system
x(t)
y(t)
z(t) = x(t)

## Slide 9: Stable Systems
A signal x(t) is said to be bounded if its magnitude does not grow without bound
, for all t
A system is bounded-input bounded-output (BIBO) stable, if for any bounded input x(t), the response y(t) is also bounded, i.e.,
implies

## Slide 10: LTI Systems
Fundamental Problem
  Determine the response to some specified input
  Can be answered in different ways
  One way: solve the differential equation describing the system subject to specified input and initial conditions
  Alternate way: exploit the linearity and time invariance of the system – Convolution Integral

## Slide 11: Convolution Integral
Linear systems governed by superposition principle
Let the responses of the system to two inputs x1(t) and x2(t) be y1(t) and y2(t) respectively
The system is linear if the response to the input x(t) = a1x1(t)+a2x2(t) is y(t) = a1y1(t)+a2y2(t)
If the input is the weighted sum of any set of signals xi(t), then x(t) = a1x1(t)+a2x2(t)+…aNxN(t)=
The output is a1y1(t)+a2y2(t)+…aNyN(t)=
The unit impulse function can be used as building blocks to represent arbitrary signals
The shifting property of the  function

## Slide 12: Convolution Integral
Output y(t) is expressed as a linear combination of the responses of the system to shifted impulse signals
  h(t,) denotes the response of a linear system to the shifted impulse (t-)
  If the system is time-invariant, then it becomes
  The above relationship is called the convolution integral of x(t) and h(t)

## Slide 13: Convolution Integral
The convolution is represented as
y(t) = x(t)* h(t)
The sufficient conditions for the convolution of two signals x(t) and h(t) to exist are :

## Slide 14: Properties of Convolution
Commutativity
Associativity
Distributivity
Example: 2.3.1, 2.3.2, 2.3.3, 2.3.4, 2.3.5

## Slide 15: Graphical Interpretation of Convolution