## Slide 1: CSE 248 Introduction to Signals and Systems
Waselul Haque Sadid, PhD
CSE Dept, East West University

## Slide 2: Definitions
Signal
Conveys information
Function of time
The way it evolves in time is what encodes the information
Examples
  Voltage or current in an electronic circuit
  Speech and music
  Bioelectric signals (e.g. ECG)

## Slide 3: Two Types of Signals
Continuous-time signals
Discrete-time signals

## Slide 4: 1. Continuous-Time Signals
Signal that has a value for all points in time
Function of time
  Written as x(t) because the signal “x” is a function of time
Commonly found in the physical world
  ex. Human speech
Displayed graphically as a line

## Slide 5: 2. Discrete-Time Signals
Signal that has a value for only specific points in time
Typically formed by “sampling” a continuous-time signal
  Taking the value of the original waveform at specific intervals in time
Function of the sample value, n
  Write as x[n]
  Often called a sequence
Commonly found in the digital world
  ex. wav file or mp3
Displayed graphically as individual values
  Called a “stem” plot
Sample number

## Slide 6: Discrete-Time ≠ Digital
Discrete-time sequences are continuous in values, but discrete only in time
Digital signals are discrete in values and discrete in time (they can only take on specific values)

## Slide 7: Systems
System
A collection of items that together performs a function
Modifies / transforms an input to give an output
Represented by
System
T{ }
x(t)
y(t) = T{x(t)}
T = input2
x(t)
y(t) = T{x(t)} = x2(t)
ex. A squaring system

## Slide 8: System Examples
Real-World Examples of Systems
Circuits
Car
  Inputs  Steering wheel, force on accelerometer and brakes
  Outputs  Position of car, velocity
Chemical processes
Electromechanical systems (motors)
Economics, stock market
Biological processes (heart)

## Slide 9: Two Types of Systems
Continuous-time systems
  Operate on continuous-time signals
  Commonly found in the physical world
  Represented mathematically using differential equations
  System parameters are defined on continuum of time
Discrete-time systems
  Operate on discrete-time signals
  ex. Computer algorithms
  Represented mathematically by difference equations
  System parameters are defined only at discrete points in time

## Slide 10: LTI System
Most engineering systems are designed to be linear and time invariant (LTI) so that they are predictable
The rest of this course focuses on LTI systems
  How to analyze
  How to use
  How to design

## Slide 11: Periodic vs Aperiodic Signals
A continuous-time signal is periodic if it satisfies x(t) = x(t + nT), n = 1, 2, 3, …
  T > 0, a constant, known as the fundamental period
  Ex. Sinusoidal functions
A real-valued sinusoidal signal can be expressed mathematically by a time-varying function of the form
  x(t) = A sin(0t + ),
  where, A is amplitude, 0 is radian frequency in rad/s,  is the initial phase angle

## Slide 12: Periodic vs Aperiodic Signals
The sum of two periodic signals may or may not be periodic
Consider two periodic signals x(t) and y(t) with fundamental periods T1 and T2
  Let the sum be z(t) = ax(t) + by(t)
  Since x(t) is periodic with period T1
  x(t) = x(t + kT1)
  Similarly, y(t) = y(t+lT2)
  z(t) = ax(t + kT1) + by(t+lT2)
  ax(t) + by(t) = ax(t + kT1) + by(t+lT2)
  T = kT1 = lT2

## Slide 13: Energy and Power Signal
Let x(t) be a real-valued signal
  Voltage across a resistance R
  Produces a current i(t) = x(t)/R
  Instantaneous power of the signal i2(t)R = x2(t)/R
  The energy expended during the incremental interval dt is x2(t)/R dt
To normalize power, assume that R = 1ohm
  Instantaneous power becomes x2(t)

## Slide 14: Energy and Power Signal
Energy over a time interval of length 2L
Total energy in the signal over the range
Average power can then be
Energy signals have zero power
Power signals have infinite energy

## Slide 15: Operations on Signals
Shifting operation
  x(t – t0) represents a time-shifted version of x(t)
  The shift in time is t0
  If t0 > 0, the signal is delayed by t0 seconds
  If t0 < 0, the signal represents an advanced replica of x(t)
  Physically, t0 cannot take on negative values

## Slide 16: Operations on Signals
Reflection operation
  x(– t) is the reflected version of x(t)
  Reversing of x(t)
Time-scaling operation
  x(t) is the scaled version of x(t)
  If || > 1, then x(t) is the compressed signal
  If || < 1, then x(t) is the expanded signal

## Slide 17: Operations on Signals
Operation should be performed in the following order
  Scaling, reflecting, shifting
Operation of scaling and reflecting is commutative
Operation of shifting and reflecting or shifting and scaling is not commutative

## Slide 18: Symmetry Properties
A signal x(t) is even signal or even symmetric if it is identical to its reflection
  i.e., x(– t) = x(t)
A signal is odd symmetric if x(– t) = – x(t)
An arbitrary signal x(t) can be expressed as the sum of even and odd signals
  x(t) = xe(t) + xo(t)
  xe(t) is the even part of x(t), xe(t) = 1/2[x(t) + x(– t)]
  xo(t) is the odd part of x(t), xo(t) = 1/2[x(t) – x(– t)]